## Slide 1: A Utility-based Multi-copy Forwarding Algorithm in Delay Tolerant Networks
Cong Liu, Yan Pan, Jun Zhang, Mingjun Xiao, Ai Chen, and Jie Wu
Presented by Yan Pan, ICCCN 2014

## Slide 2: Outline
DTN preliminaries
Model and motivation
Our solution: the MOUF algorithm
Simulation

## Slide 3: Delay tolerant network (DTN)
A DTN is a self-organized network of short-distance communication devises.
Messages are forwarded by predicting and using node mobility

## Slide 4: Message forwarding in DTNs
Two contradictory objectives:
  High delivery performance: achieved by improving the quality and quantity of the forwarding nodes.
  Low forwarding overhead: via reducing the total number of forwarding nodes.

## Slide 5: Outline
DTN preliminaries
Model and motivation
Our solution: the MOUF algorithm
Simulation

## Slide 6: Model
Let N be the set of all nodes
Ii,j be the average inter-contact time between nodes i and j.
  Each node i locally computes Ii,js over a warm-up period.
  If nodes i and j have no contact, Ii,j = ∞

## Slide 7: Model
Each message has a source, a dest, a TTL
Multi-copy forwarding of each message:
  different copies are forwarded independently
  Each copy have no knowledge of the others
Node charges for each copy it forwards

## Slide 8: Motivation
DTN forwarding algorithms using simple metrics
  delivery rate, delay and forwarding cost
These metrics can be contradictory
  An algorithm that maximize delivery rate might create excessive forwarding cost
  An algorithm that bounds forwarding cost inappropriately might results in low delivery rate.
We want user-preferred trade-offs

## Slide 9: Outline
DTN preliminaries
Model and motivation
Our solution: the MOUF algorithm
Simulation

## Slide 10: Our solution: a utility-based metrics
Utility function
  B: initial benefit: maximum benefit
  t: delay
  c: sum of forwarder charges
  ∆ : benefit delay, trade-off between t and c
For failed-to-deliver messages

## Slide 11: A simplified forwarding scheme
The forwarding tree
  Copies on a branch Have no information about copies on other branches

## Slide 12: A simplified forwarding scheme
Key forwarder
  One per message
  Other forwarders can only forward to dest
  Key forwarder keep looking for better j with smaller Ij,d, which if found, become the new key forwarder
Only the key forwarder
  Forward to increase the utility of the message
  It has the full knowledge of

## Slide 13: A simplified forwarding scheme
Compare the key-forwarder scheme to the 2-hop forwarding scheme:
  In 2-hop forwarding: the key-forwarder is always the source
  In our scheme: the key-forwarder is always the nodes (known so far) that has the smallest inter-contact time with the dest

## Slide 14: Utility maximization
The key-forwarder makes forwarding decision to maximize the expected utility:
  The joint delay of all copies, locally estimated by the key forwarder:
    t’ : the the time elapsed since the creation of the message
    : the estimated delay starting from the current time

## Slide 15: Utility maximization
Whenever the key-forwarder k of message m is connected with another node i, there are two options:
  k forwards m to i, the expected utility:
  k does not forward

## Slide 16: The MOUF algorithm

## Slide 17: The MOUF algorithm

## Slide 18: Outline
DTN preliminaries
Model and motivation
Our solution: the MOUF algorithm
Simulation

## Slide 19: Simulation
We perform simulations on 7 real traces

## Slide 20: Simulation results

## Slide 21: Thank you
Questions are welcome: liucong3@mail.sysu.edu.cn