## Slide 1: Image Segmentation Using Region Growing and Shrinking
Computer Graphics and Image Processing
Professor : Dr. Longin Jan Latecki
Siddu@temple.edu

## Slide 2
Contents
Brief introduction to Image segmentation
Types of Image segmentation
Region growing and Shrinking (split /merge ) method
Applications of Image segmentation
Results

## Slide 3
Introduction
The shape of an object can be described in terms of:
Its boundary – requires image edge detection
The region it occupies – requires image segmentation in homogeneous regions, Image regions generally have homogeneous characteristics (e.g. intensity, texture)

## Slide 4
Introduction- cont.d
The goal of Image Segmentation is to find regions that represent objects or meaningful parts of objects. Major problems of image segmentation are result of noise in the image.
An image domain X must be segmented in N different regions R(1),…,R(N)
The segmentation rule is a logical predicate of the form P(R)

## Slide 5
Introduction- cont.d
Image segmentation partitions the set X into the subsets R(i), i=1,…,N having the following properties
  X = i=1,..N U R(i)
  R(i) ∩ R(j) = 0 for I ≠ j
  P(R(i)) = TRUE for i = 1,2,…,N
  P(R(i) U R(j)) = FALSE for i ≠ j

## Slide 6
Introduction- cont.d
The segmentation result is a logical predicate of the form P(R,x,t)
x is a feature vector associated with an image pixel
t is a set of parameters (usually thresholds) A simple segmentation rule has the form:
P(R) : I(r,c) < T

## Slide 7
Introduction- cont.d
In the case of color images the feature vector x can be three RGB image components {IR(r,c),IG(r,c),IB(r,c)
A simple segmentation rule may have the form:
P(R,x,t) : (IR(r,c) <T(R)) && (IG(r,c)<T(G))&&
(IB(r,c) < T(B))

## Slide 8
Introduction- cont.d
A region is called connected if : …….
A pixel (x,y) is said to be adjacent to the pixel (a,b) if it belongs to its immediate neighbourhood
The 4-neighbourhood of a pixel (x,y) is the set that includes its …..
The 8-neighbourhood of (x,y) is a superset of the 4-neighbourhood and contains the …..

## Slide 9
Types
By Histogram Thresholding
By Region Growing and Shrinking
By Clustering in the color space

## Slide 10
Region Growing
A simple approach to image segmentation is to start from some pixels (seeds) representing distinct image regions and to grow them, until they cover the entire image
For region growing we need a rule describing a growth mechanism and a rule checking the homogeneity of the regions after each growth step

## Slide 11
Region Growing – cont.d
The growth mechanism – at each stage k and for each region Ri(k), i = 1,…,N, we check if there are unclassified pixels in the 8-neighbourhood of each pixel of the region border
Before assigning such a pixel x to a region Ri(k),we check if the region homogeneity:
P(Ri(k) U {x}) = TRUE , is valid

## Slide 12
Region Growing – cont.d
The arithmetic mean m and standard deviation sd of a class Ri having n pixels:
M = (1/n)(r,c)€R(i) ∑ I(r,c)
s.d = Square root((1/n)(r,c)€R(i) ∑[I(r,c)-M]2)
Can be used to decide if the merging of the two regions R1,R2 is allowed, if
|M1 – M2| < (k)s.d(i) , i = 1, 2 , two regions are merged

## Slide 13
Region Growing – cont.d
Homogeneity test: if the pixel intensity is close to the region mean value
|I(r,c) – M(i)| <= T(i)
Threshold Ti varies depending on the region Rn and the intensity of the pixel I(r,c).It can be chosen this way:
T(i) = { 1 – [s.d(i)/M(i)] } T

## Slide 14
Split / Merge
The opposite approach to region growing is region shrinking ( splitting ).
It is a top-down approach and it starts with the assumption that the entire image is homogeneous
If this is not true , the image is split into four sub images
This splitting procedure is repeated recursively until we split the image into homogeneous regions

## Slide 15
Split / Merge
If the original image is square N x N, having dimensions that are powers of 2(N = 2n):
All regions produced but the splitting algorithm are squares having dimensions M x M , where M is a power of 2 as well (M=2m,M<= n).
Since the procedure is recursive, it produces an image representation that can be described by a tree whose nodes have four sons each
Such a tree is called a Quadtree.

## Slide 16
Split / Merge
Quadtree
R0
R1
R2
R3
R0
R1
R00
R01
R02
R04

## Slide 17
Split / Merge
Splitting techniques disadvantage, they create regions that may be adjacent and homogeneous, but not merged.
Split and Merge method – It is an iterative algorithm that includes both splitting and merging at each iteration:

## Slide 18
Split / Merge
If a region R is inhomogeneous (P(R)= False) then is split into four sub regions
If two adjacent regions Ri,Rj are homogeneous (P(Ri U Rj) = TRUE), they are merged
The algorithm stops when no further splitting or merging is possible

## Slide 19
Split / Merge
The split and merge algorithm produces more compact regions than the pure splitting algorithm

## Slide 20
Applications
3D – Imaging : A basic task in 3-D image processing is the segmentation of an image which classifies voxels/pixels into objects or groups. 3-D image segmentation makes it possible to create 3-D rendering for multiple objects and perform quantitative analysis for the size, density and other parameters of detected objects.
Several applications in the field of Medicine like magnetic resonance imaging (MRI).

## Slide 21
Results – Region grow

## Slide 22
Results – Region Split

## Slide 23
Results – Region Split and Merge

## Slide 24
Results – Region growing

## Slide 25
Results – Region Split

## Slide 26
Results – Region Split and Merge

## Slide 27
References
“Digital Image Processing” – Algorithms and Application , A multimedia approach.
Prof. Ioannis Pitas
Computer Vision and Image Processing: A Practical Approach
CVIP Tools software

## Slide 28
Thank You