## Slide 1
Range Image Processing
Archana Gupta

## Slide 2: What are range images ?
Range images are a special class of digital images where each pixel expresses the distance between a known reference frame and a visible point in the scene.
They are also known as depth images.

## Slide 3: Application of range images
Reverse engineering
Collaborative design
Inspection
Special effects, games & virtual worlds
Dissemination of museum artifacts
Medicine
Home shopping

## Slide 4: Steps towards Range Image processing
Data collection
Data registration
Data Modeling (geometry, texture and lighting

## Slide 5: Data collection
(a)
(b)

## Slide 6: Measurement principle
Every pixel on the sensor samples the amount of modulated light reflected by objects in the scene. The phase shift between the emitted light and the returning signal determines the distance to the objects in the scene. This is illustrated by fig (a) .
A range image obtained from a scanner in fig (a) is a collection of points with regular spacing as shown in fig (b).

## Slide 7: Problem with such data acquisition
Some calibration has to be performed in order to get rid of the distortions and misalignments of the optical lens and sensor. As a result some data preprocessing is performed.

## Slide 8: Preprocessing
The uncertainty value generated by the sensor as a function of measured amplitude is used to filter out inaccurate data points.
A grid around the viewing range of sensor is decomposed into cells and each cell must contain a minimum no of data points to be considered occupied.

## Slide 9: B. Data registration
Registration involves having features in multiple scenes exactly match each other in location.
In other words the key step here is to find a spatial transformation (linear in nature) such that a similarity metric between two or more images taken at different times and from different sensors or different viewpoints, achieves its maximum.

## Slide 10: C. Data Modeling (geometry, texture and lighting)
Surface Reconstruction
Size of CCD matrix 124 X 160
Translate x and y so that CCD center aligns with origin of the coordinate system

## Slide 12: Surface reconstruction cont…
Finding angles

## Slide 13: Surface reconstruction cont…
Finding the real points

## Slide 14
Mesh creation & simplification

## Slide 15
The faces are found and the mesh is created using the patch command in matlab.
The mesh is then simplified. There are many mesh simplification software available online. I made use of QSlim.

## Slide 16: Mesh simplification algorithms
Vertex clustering: spatially partitions vertices and unifies vertices in same cluster.
Vertex decimation: selects unimportant vertices (based on local shape heuristics), remove them and retriangulate resulting holes.
Iterative Edge contraction: ranks edges and collapses one with least resulting error.

## Slide 17: QSlim details
QSlim uses an algorithm based on iterative edge contraction and quadric error metrics.

## Slide 18: Quadric Error metrics
Each vertex has (conceptual) set of planes.
Vertex error = sum of squared distances to planes.
Combine sets when contracting vertex pair.

## Slide 19: Measuring error with Quadrics

## Slide 20: Measuring error with Quadrics cont..

## Slide 21: Mesh smoothing via mean filtering

## Slide 24: Results

## Slide 25: Initial Image

## Slide 26: Image after filtering

## Slide 27: 3D Cloud of image

## Slide 28: 3D mesh

## Slide 29: Mesh with 10000 faces

## Slide 30: Mesh with 800 faces

## Slide 31: Mesh with 500 faces

## Slide 32: Mesh after mean smoothing 4 iterations

## Slide 33: Mesh after mean smoothing 10 iterations

## Slide 34: Conclusions
The mesh produced after converting image coordinates to real world coordinates is quite impressive.
The Qslim software works very well in simplifying the mesh to the number of triangle faces required by the user.
Finally the Mean filter for averaging face normals algorithm seems to do a good job at defining the ball but distorts the wall edges.

## Slide 35: References
Thanks to Dr Latecki for his invaluable guidance
http://www.csem.ch/detailed/pdf/p_531_SR-2_Preliminary-0355.pdf
http://asl.epfl.ch/aslInternalWeb/ASL/publications/uploadedFiles/2004iros_weingarten.pdf
Introductory Techniques for 3-D Computer Vision by Emanuele Trucco and Alessandro Verri
http://graphics.cs.uiuc.edu/~garland/software/qslim.html
http://www.u-aizu.ac.jp/labs/sw-sm/Yagou/gmp02yob.pdf